## Slide 1: Code Converters
A code converter is a logic circuit that changes data presented in one type of binary code to another type of binary code, such as BCD to binary, BCD to 7segment, binary to BCD, BCD to XS3, binary to Gray code, and Gray code to binary.

## Slide 2: BCD-to-Excess-3 Code converter
BCD is a code for the decimal digits 0-9
Excess-3 is also a code for the decimal digits

## Slide 3: Specification of BCD-to-Excess3
Inputs: a BCD input, A,B,C,D with A as the most significant bit and D as the least significant bit.
Outputs: an Excess-3 output W,X,Y,Z that corresponds to the BCD input.
Internal operation – circuit to do the conversion in combinational logic.

## Slide 4: Formulation of BCD-to-Excess-3
Excess-3 code is easily formed by adding a binary 3 to the binary or BCD for the digit.
There are 16 possible inputs for both BCD and Excess-3.
It can be assumed that only valid BCD inputs will appear so the six combinations not used can be treated as don’t cares.

## Slide 5: Optimization – BCD-to-Excess-3
Lay out K-maps for each output, W X Y Z
A step in the digital circuit design process.

## Slide 6: Placing 1 on K-maps
Where are the minterms located on a K-Map?

## Slide 7: Expressions for W X Y Z
W(A,B,C,D) = Σm(5,6,7,8,9) +d(10,11,12,13,14,15)
X(A,B,C,D) = Σm(1,2,3,4,9) +d(10,11,12,13,14,15)
Y(A,B,C,D) = Σm(0,3,4,7,8) +d(10,11,12,13,14,15)
Z(A,B,C,D) = Σm(0,2,4,6,8) +d(10,11,12,13,14,15)

## Slide 8: Minimize K-Maps
W minimization
Find W = A + BC + BD

## Slide 9: Minimize K-Maps
X minimization
Find X = BC’D’+B’C+B’D

## Slide 10: Minimize K-Maps
Y minimization
Find Y = CD + C’D’

## Slide 11: Two level circuit implementation
Have equations
  W = A + BC + BD = A + B(C+D)
  X = B’C + B’D + BC’D’ = B’(C+D) + BC’D’
  Y = CD + C’D’
  Z = D’
Factoring out (C+D) and call it T
Then T’ = (C+D)’ = C’D’
  W = A + BT
  X = B’T + BT’
  Y = CD + T’
  Z = D’

## Slide 12: Create the digital circuit
Implementing the second set of equations where T=C+D results in a lower gate count.
This gate has a fanout of 3

## Slide 13: FOUR BIT BINARY TO GRAY CODE CONVERTER –DESIGN (1)…
TRUTH TABLE:
MSB
0
+
1
+
1
+
0
+
1
0
1
0
1
1
Binary code
Gray code
INPUT ( BINARY) |  |  |  |  | OUTPUTS (GRAY CODE) |  |  | 
B3 | B2 | B1 | B0 |  | G3 | G2 | G1 | G0
0 | 0 | 0 | 0 |  | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 |  | 0 | 0 | 0 | 1
0 | 0 | 1 | 0 |  | 0 | 0 | 1 | 1
0 | 0 | 1 | 1 |  | 0 | 0 | 1 | 0
0 | 1 | 0 | 0 |  | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 |  | 0 | 1 | 1 | 1
0 | 1 | 1 | 0 |  | 0 | 1 | 0 | 1
0 | 1 | 1 | 1 |  | 0 | 1 | 0 | 0
1 | 0 | 0 | 0 |  | 1 | 1 | 0 | 0
1 | 0 | 0 | 1 |  | 1 | 1 | 0 | 1
1 | 0 | 1 | 0 |  | 1 | 1 | 1 | 1
1 | 0 | 1 | 1 |  | 1 | 1 | 1 | 0
1 | 1 | 0 | 0 |  | 1 | 0 | 1 | 0
1 | 1 | 0 | 1 |  | 1 | 0 | 1 | 1
1 | 1 | 1 | 0 |  | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 |  | 1 | 0 | 0 | 0

## Slide 14: FOUR BIT BINARY TO GRAY CODE CONVERTER –DESIGN (2)…
Simplification using K-maps:

## Slide 15
FOUR BIT BINARY TO GRAY CODE CONVERTER –DESIGN (3)
Logic Diagram:

## Slide 16: COMPARATORS
Comparator is a combinational logic circuit that compares the magnitudes of two binary quantities to determine which one has the greater magnitude.
In other word, a comparator determines the relationship of two binary quantities.
A exclusiveOR gate can be used as a basic comparator.

## Slide 17
If two input bits are not equal, its output is a 1. But if
two input bits are equal, its output is a 0.
So exclusiveOR gate can be used as a 2bit Comparator.

## Slide 18: 1 bit comparator
Truth Table
A B f (A>B) f (A=B) f (A<B)
0 0 0 1 0
1 0 1 0 0
0 1 0 0 1
1 1 0 1 0

## Slide 19: 1 bit comparator
And now we find the equations using K-maps each for f (A>B), f (A=B) and f (A<B)

## Slide 22: 2 bit comparator
A B f (A>B) f (A=B) f (A<B)
00 00 0 1 0
01 00 1 0 0
10 00 1 0 0
11 00 1 0 0
00 01 0 0 1
01 01 0 1 0
10 01 1 0 0
11 01 1 0 0
00 10 0 0 1
01 10 0 0 1
10 10 0 1 0
11 10 1 0 0
00 11 0 0 1
01 11 0 0 1
10 11 0 0 1
11 11 0 1 0

## Slide 23: 2 bit comparator

## Slide 24: 2 bit comparator

## Slide 25: 2 bit comparator

## Slide 26: 4 bit comparator
Start with most significant bit in each number to determine the inequality of 4-bit binary numbers A and B
Output A<B will be HIGH if A3=0, and B3=1
Output A>B will be HIGH if A3=1, and B3=0
If A3=0, and B3=0 or A3=1, and B3=1, then examine the next lower order bit position for an inequality.Only when all bits of A=B, output A=B will be HIGH

## Slide 27: 4 bit comparator
The general procedure used in comparator:
Start with the highest-order bits (MSB)
When an inequality is found, the relationship of the 2
numbers is established, and any other inequalities in lower-
order positions must be ignored
THE HIGHEST ORDER INDICATION MUST TAKE
PRECEDENCE

## Slide 28: 4 bit comparator
In addition, it also has three cascading inputs:
These inputs provides a means for expanding the comparison operation by cascading two or more 4bit comparator.
To expand the comparator, the A<B, A=B, and A>B outputs of the lowerorder comparator are connected to the corresponding cascading inputs of the next higherorder comparator.

## Slide 32: Decoder
  Accepts a value and decodes it
    Output corresponds to value of n inputs
  Consists of:
    Inputs (n)
    Outputs (2n , numbered from 0  2n - 1)
    Selectors / Enable (active high or active low)

## Slide 33: The truth table of 2-to-4 Decoder

## Slide 34: 2-to-4 Decoder

## Slide 35: 2-to-4 Decoder

## Slide 36: The truth table of 3-to-8 Decoder
A2 | A1 | A0 | D0 | D1 | D2 | D3 | D4 | D5 | D6 | D7
0 | 0 | 0 | 1 |  |  |  |  |  |  | 
0 | 0 | 1 |  | 1 |  |  |  |  |  | 
0 | 1 | 0 |  |  | 1 |  |  |  |  | 
0 | 1 | 1 |  |  |  | 1 |  |  |  | 
1 | 0 | 0 |  |  |  |  | 1 |  |  | 
1 | 0 | 1 |  |  |  |  |  | 1 |  | 
1 | 1 | 0 |  |  |  |  |  |  | 1 | 
1 | 1 | 1 |  |  |  |  |  |  |  | 1

## Slide 37: 3-to-8 Decoder

## Slide 38: 3-to-8 Decoder with Enable

## Slide 39: Decoder Expansion
Decoder expansion
  Combine two or more small decoders with enable inputs to form a larger decoder
  3-to-8-line decoder constructed from two 2-to-4-line decoders
    The MSB is connected to the enable inputs
    if A2=0, upper is enabled; if A2=1, lower is enabled.

## Slide 40: Decoder Expansion